## Slide 1: Analyzing a Development Site
for Low Impact Development design

## Slide 2: LID Design Guide
Analyze your project
  Select LID options
Design site and document drainage
  Show how criteria are met
Specify preliminary design details
  Integrate LID with paving and landscaping
Iterate
Page 35

## Slide 3: LID Design Guide
Analyze your project
  Select LID options
Design site and document drainage
  Show how criteria are met
Specify preliminary design details
  Integrate LID with paving and landscaping
Iterate

## Slide 4: Strategies, Applicability, Design
Optimize the site layout
Use pervious surfaces
Disperse runoff
Store runoff and use it later
Use bioretention (or other facilities)
Page 36

## Slide 5: Optimize the Site Layout
Protect Watercourses and Drainage
Preserve Open Space
Cluster Buildings
Minimize Pavement Widths
Minimize Parking
APPLICABILITY

## Slide 6: Pervious Pavement
Expensive to build
Durability and maintenance issues
Best for:
  Flat sites with limited access to drainage
    No need for drainage pipes or structures
  On well-drained, competent soils
  Where traffic is limited
  For aesthetic reasons
  To avoid thresholds
APPLICABILITY

## Slide 7: Pervious Pavement Design Issues
Subgrade
  No compaction or minimal compaction
  Captures and holds runoff at interface
  Avoid surfacing of runoff
No subdrain
  Or minimum 3 inches above soil
APPLICABILITY

## Slide 8: Disperse Runoff
Extensive flat, landscaped areas
  Next to buildings
  Downgradient from paved areas
Impervious:Pervious ratios
  2:1 if treatment only criteria apply
  1:1 if flow-control (hydromodification management) criteria apply
APPLICABILITY

## Slide 9: Harvesting and Reuse
Where there is an industrial demand for non-potable water
  Concrete plants
  Washing
Projects emphasizing water conservation and sustainability
  LEED certification
Where there is intense occupancy and good facility management
  High rises
  Public facilities
APPLICABILITY

## Slide 10: Bioretention
Applicable to nearly any development site
Can reliably treat and manage runoff in small footprint
Achieves some infiltration and evapotranspiration
Flow-through planter can be used if infiltration is infeasible
APPLICABILITY

## Slide 11: Example Development Site
Thanks to:
Signature Properties dk Consulting City of Lafayette

## Slide 12: Opportunities and Constraints
DESIGN

## Slide 13: Opportunities and Constraints
DESIGN
1%

## Slide 14: Opportunities and Constraints
Fill 8.5 to 15 feet deep
Silty clay to clayey sand (Group “D”)
DESIGN

## Slide 15: Opportunities and Constraints
Densely developed townhome project
DESIGN

## Slide 16: Opportunities and Constraints
Landscaped areas around buildings and central plaza/green space
DESIGN

## Slide 17: Applying the Strategies
DESIGN
Optimize the site layout
Use pervious surfaces
Disperse runoff
Store runoff and use it later
Use bioretention (or other facilities)