This brochure is one of a series of pamphlets describing storm drain protection measures for specific types of construction industry activities.  Other pamphlets include:

General Construction and

Site Supervision

Landscaping, Gardening and

Pool Maintenance

Painting and Application of

Solvents and Adhesives

Fresh Concrete and Mortar

Application

Roadwork and Paving

Earth-Moving Activities

Heavy Equipment Operation

For more information about the county-wide storm drain protection program and additional brochures, call:

Contra Costa

Clean Water Program

255 Glacier Drive

Martinez, CA  94553

1-800-NO-DUMPING

Spill Response Agencies

- Dial 911

- Governor’s Office of Emergency Services Warning Center

(800)  852-7550 (24 hours)

Local Pollution Control Agencies

| Contra Costa Clean Water Program | (925) 313-2360 |
| --- | --- |
| City of Antioch | (925) 779-7097 |
| City of Brentwood | (925) 516-5169 |
| City of Clayton | (925) 673-7308 |
| City of Concord | (925) 671-3394 |
| Contra Costa County | (925) 313-2259 |
| Town of Danville | (925) 314-3342 |
| City of El Cerrito | (510) 215-4367 |
| City of Hercules | (510) 799-8242 |
| City of Lafayette | (925) 299-3240 |
| City of Martinez | (925) 372-3563 |
| Town of Moraga | (925) 376-2590 |
| City of Oakley | (925) 625-7003 |
| City of Orinda | (925) 253-4231 |
| City of Pinole | (510) 741-2065 |
| City of Pittsburg | (925) 252-4110 |
| City of Pleasant Hill | (925) 671-5261 |
| City of Richmond | (510) 231-3011 |
| City of San Pablo | (510) 215-3066 |
| City of San Ramon | (925) 973-2800 |
| City of Walnut Creek | (925) 943-5899 |

EARTH MOVING     ACTIVITIES

Best Management

Practices for the

Construction Industry

Contra Costa

Clean Water Program

Storm Drain

Pollution Prevention:

It’s Up to Us

In Contra Costa County, storm drains flow directly to local creeks, San Francisco Bay, and the delta without treatment.  Storm water pollution is a serious problem for wildlife dependent on our waterways and for the people who live near polluted streams or baylands.  Some common sources of this pollution include spilled oil, fuel, and fluids from vehicles and heavy equipment; construction debris; landscaping runoff containing pesticides or weed killers; and materials such as used motor oil, antifreeze, and paint products that people pour or spill into a street or storm drain.  Eighteen cities, the County, and the County Flood Control District have joined together to educate local residents and businesses to fight storm drain pollution.  We hope you will join us by using the practices described in this pamphlet.

Who should use this brochure?

Bulldozer, Backhoe, and Grading Machine Operators

Dump Truck Drivers

Site Supervisors

General Contractors

Home Builders

Developers

Storm Drain Pollution from Earth-Moving Activities

Soil excavation and grading operations loosen large amounts of soil that can flow or blow into storm drains if handled improperly.  Soil erodes due to a combination of decreased soil stability, increased runoff, and increased flow velocity.  Some of the most effective erosion control practices reduce the amount of runoff crossing a site and slow the flow with check dams and roughened ground surfaces.

What Can You Do?

During Construction

- Remove existing vegetation only when absolutely necessary.

- Consider planting temporary vegetation or implement other appropriate erosion controls on slopes where construction is not immediately planned.

- Protect downslope drainage courses, streams, and storm drains with silt fences or other controls to intercept and low the flow of sediment laden discharges.

- Use check dams or ditches to divert runoff around excavations.

- Cover stockpiles and excavated soil with secured tarps or plastic sheeting.

- Stockpile erosion controls during the wet season.

General Business Practices

- Schedule excavation and grading work for dry weather.

- Perform major equipment repairs away from the job site.

- When refueling or vehicle/equipment maintenance must be done on site, designate a location away from storm drains.

- Do not use diesel oil to lubricate equipment or parts.

Detecting contaminated soil or groundwater

It is essential that all contractors and subcontractors involved in excavation and grading know what to look for in detecting contaminated soil or groundwater.  See Blueprint for a Clean Bay, a construction best management practices guide available from Contra Costa Clean Water Program, for details.

Watch for any of these conditions:

- Unusual soil conditions, discoloration, or odor

- Abandoned underground tanks

- Abandoned wells

- Buried barrels, debris, or trash

If contamination is suspected, call the appropriate local agency for further guidance (see reverse).