# Stormwater Facility Operation and Maintenance Fact Sheet

## Bioretention Areas

These facilities remove pollutants primarily by filtering runoff slowly through an active layer of soil. Routine maintenance is needed to ensure that flow is unobstructed, that erosion is prevented, and that soils are held together by plant roots and are biologically active. Typical maintenance consists of the following:

Inspect inlets for channels, exposure of soils, or other evidence of erosion. Clear any obstructions and remove any accumulation of sediment. Examine rock or other material used as a splash pad and replenish if necessary.

Inspect outlets for erosion or plugging.

Inspect side slopes for evidence of instability or erosion and correct as necessary.

Observe soil at the bottom of the swale or filter for uniform percolation throughout. If portions of the swale or filter do not drain within 48 hours after the end of a storm, the soil should be tilled and replanted. Remove any debris or accumulations of sediment.

Confirm that check dams and flow spreaders are in place and level and that channelization within the swale or filter is effectively prevented.

Examine the vegetation to ensure that it is healthy and dense enough to provide filtering and to protect soils from erosion. Replenish mulch as necessary, remove fallen leaves and debris, prune large shrubs or trees, and mow turf areas. When mowing, remove no more than 1/3 height of grasses. Confirm that irrigation is adequate and not excessive. Replace dead plants and remove noxious and invasive vegetation.

Abate any potential vectors by filling holes in the ground in and around the swale and by insuring that there are no areas where water stands longer than 48 hours following a storm. If mosquito larvae are present and persistent, contact the Contra Costa Mosquito and Vector Control District for information and advice. Mosquito larvicides should be applied only when absolutely necessary and then only by a licensed individual or contractor.