## Slide 1: Municipal Regional Permit Provision C.6
Dan Cloak, P.E. Principal Dan Cloak Environmental Consulting

## Slide 2: Provision C.6 Overview
Which projects are required to implement BMPs?
What BMPs are required?
What projects must municipalities inspect?
What must be inspected?
What happens if a violation is found?
What must be tracked and documented?
What must be reported?

## Slide 3: What Projects Require BMPs?
Municipalities must require all construction sites to have site-specific, and seasonally and phase-appropriate BMPs.

## Slide 4: What BMPs are Required?
Site-Specific BMPs in Six Categories
  Erosion Control
  Run-on and Run-off Control
  Sediment Control
  Active Treatment Systems (if needed)
  Good Site Management
  Non-Stormwater Management
Same as Construction General Permit

## Slide 5: What BMPs are Required?
References for BMPs
  California BMP Handbooks (CASQA)
  Caltrans Stormwater Quality Handbooks
  RWQCB Erosion and Sediment Control Field Manual (2002)
  New BMPs

## Slide 6: What BMPs are Required?
Municipalities must:
  Review contractors’ SWPPP or erosion/pollution control plan to confirm appropriate BMPs are planned
  Provide outreach materials
  For sites disturbing an acre or more:
    Verify filing for Construction General Permit
    By September 1, remind owners/ developers to prepare for wet season

## Slide 7: Inspections—When and Where
Monthly inspections
  All sites disturbing an acre or more
  “High Priority” sites, based on:
    Soil erosion potential
    Slope
    Project size and type
    Proximity/sensitivity of waters
    If Municipality or Water Board say so

## Slide 8: Inspections — What
Inspections are for:
  Compliance with SWPPPs, etc.
  Adequacy of BMPs
  Evidence of discharge
  Actual or potential illicit connections
  Education
All inspections are recorded
  Electronic database or tabular format

## Slide 9: Inspection Tracking
Project Info
Inspection Info
BMP Info
  6 categories
  4 columns
  Comments
Enforcement

## Slide 10: Enforcement
Required by Permit
Progressive (Levels 1- 4)
Specified in local Enforcement Response Plan

## Slide 11: Enforcement Level One
Verbal Warning or Warning Notice for:
  Exposed pollutant sources
  Evidence of past discharge
  Inadequate BMPs
Follow-up
  Log the incident
    Example: Check “Needs Attention” on Construction Site Inspection Report
  Re-inspect if needed

## Slide 12: Enforcement Level Two
Notice of Violation for:
  Active pollutant discharge, or
  Failure to comply with warning
Remediation plan and schedule
  May also use Clean/Abate, Cease/Desist, or Stop Work order
  Timely correction (before next rain)
  Correct within 10 days or provide rationale
  Document resolution

## Slide 13: Enforcement Level Three
Major Violation
  Discharge of hazardous materials
  Pattern of noncompliance
  Failure to respond to notice of violation
Remediation plan and schedule
  Citation
  Cost recovery
  Negotiated settlement

## Slide 14: Enforcement Level Four
Legal Action
  Failure to respond to Level Three actions
Referral may be to:
  City Attorney and/or
  Contra Costa County District Attorney
  Emergency responders
  Regional Water Board
  California Dept. Fish and Game

## Slide 15: Staff Training
Training every other year
  Correct uses of BMPs
  BMP installation and maintenance
  Permit requirements
  Local requirements
  Enforcement Response Plans
Include in Annual Report
  Topics covered
  Percentage of inspectors attending