## Slide 1: Implementing MRP Provision C.3
Stormwater NPDES Compliance
For New Developments

## Slide 2: Overview
Stormwater NPDES Compliance for New Developments

## Slide 3: C.3 Regulatory History
1987 | Congress adds Section 402(p) to Clean Water Act
1990 | USEPA regulations require states to issue stormwater NPDES permits to large municipalities
1990 | Regional Water Board issues first Bay Area stormwater NPDES permits
2000 | State Water Resources Control Board “Bellflower decision” confirms municipalities must require new developments to treat runoff
OVERVIEW

## Slide 4: C.3 Regulatory History
2003 | Regional Water Board adds Provision C.3 to stormwater permit for Contra Costa municipalities
2005 | C.3 implementation begins for projects creating or replacing an acre or more of impervious area
2006 | Water Board adopts Contra Costa’s Hydrograph Modification Management Plan and requirements take effect. C.3 threshold for treatment requirements drops from one acre to 10,000 square feet of impervious area
OVERVIEW

## Slide 5: C.3 Regulatory History
2009 | Municipal Regional Permit adopted, including LID requirements. Threshold for some land uses lowered to 5,000 SF of impervious area. Contra Costa develops current HMP sizing factors and calculator.
2011 | MRP amended, including “Special Projects” categories. LID requirements take effect, including feasibility tests for infiltration and harvesting/reuse.
2013 | C.3 includes “major issues” for MRP reissuance, scheduled for late 2014
OVERVIEW

## Slide 6: C.3 in a nutshell
Projects subject to C.3 must:
Minimize imperviousness
Control potential pollutant sources
Use LID to treat stormwater before discharge
Match runoff peaks and durations to pre-project conditions
  Projects ≥ 1 acre impervious area, where downstream beneficial uses could be affected
Maintain treatment and flow-control facilities.
OVERVIEW

## Slide 7: C.3 & Development Review
OVERVIEW
Pre-Application
Meeting
Completed
Application
“Deemed
Complete”
Section
Review
CEQA
Review
Conditions of Approval
Planning
Commission
Detailed
Design
Plan Check
Permits
to
Build

## Slide 8: Path to Compliance
Pre-application meeting
Review Guidebook
Prepare a Stormwater Control Plan
Prepare detailed project design
C.3 checklist on project plans
Prepare Operation & Maintenance Plan
Maintain facilities during construction
Final O&M Plan, transfer responsibility
Maintain facilities in perpetuity
OVERVIEW
Page 4

## Slide 9: Tools and Resources
OVERVIEW

## Slide 10: Applicability
Stormwater NPDES Compliance for New Developments

## Slide 11: In Summary…
APPLICABILITY
All projects | Site design measures and source controls
≥2500 SF | Include at least one of six LID measures
≥(5,000 SF) ≥10,000 SF | (For parking lots, auto service, restaurants) Treat flows to numeric standard
≥1 acre | Hydromodification Management
Page 4

## Slide 12: Applying the Thresholds
Grandfathering and new approvals
Phased Projects
  Apply threshold to the whole of the action
  Guard against piecemealing
  Require the appropriate level of detail
Subdivision Map Approvals
  Estimate future impervious area
  Type, size, location, final ownership of treatment and flow-control facilities
  Mechanism to ensure future implementation
  See the Policy on C.3 for Subdivisions
Page 6
APPLICABILITY

## Slide 13: Threshold Arcana
What if the project reduces the amount of impervious surface?
What about a 6,000 SF project with two parking spaces?
Does pervious pavement count?
Does pavement replacement count?
Are swimming pools impervious?
Is gravel impervious?
Are public improvements included?
APPLICABILITY

## Slide 14: The 50% Rule
APPLICABILITY
OLD
NEW
Criterion in previous permit (2003-2009): Project results in an increase of or replacement of 50% or more of existing development
MRP criterion: Project results in alteration of more than 50% of the previously existing development
Existing Development
OLD
NEW

## Slide 15: LID CONCEPTUAL DESIGN
Stormwater NPDES Compliance for New Developments

## Slide 16: Conventional Urban Drainage
Impervious surfaces: roofs and pavement
Catch basins and piped drainage
“Collect and convey” design objective
LID CONCEPTS

## Slide 17: Drainage Impacts
LID CONCEPTS
Site Scale | Watershed and Stream Scale
Higher peak flows | Flooding and scouring of stream beds
Lower time of concentration | Flash flows
Runoff from small storms | Discharge when runoff did not previously occur
Increased runoff durations | Stream erosion at moderate stream flow rates
Greater runoff volumes | Higher pollutant loading
Greater runoff energy | Conveys trash and gross pollutants to streams
Decreased infiltration | Lower and less frequent stream base flow
Dry weather discharges | High pollutant concentrations during low flows
Notes: The pictures relate to items #1, #4, and #6 in the table.

## Slide 18: LID Design Objectives
Watershed and Stream Scale | Site scale
Reduce peak flows | Detain runoff on site
Increase time of concentration | Slow runoff from leaving site
No runoff from small storms | Infiltrate, evapotranspirate and reuse
Reduce duration of moderate flows | Let runoff seep away very slowly
Reduce runoff volume | Infiltrate and reuse where possible
Reduce runoff energy | Detain and slow flows
Increase groundwater storage and stream base flows | Facilitate infiltration
Reduce pollutants in runoff | Detain and filter runoff
Protect against spills and dumping | Disconnect drainage and filter runoff
LID CONCEPTS

## Slide 19: LID Design Process
LID CONCEPTS
Analyze Project for LID
Develop and Document LID Drainage Design
Specify LID Preliminary Design Details
Coordinate with Site Design and Landscape Design
Page 35

## Slide 20: Analyzing a Project for LID
Five LID Strategies
Optimize the site layout
Use pervious surfaces
Disperse runoff
Store runoff and use it later
Direct runoff to bioretention facilities
LID CONCEPTS

## Slide 21: 1. Optimize the Site Layout
Define the development envelope
Set back from creeks, wetlands, and riparian habitats
Preserve significant trees
Minimize grading
LID CONCEPTS

## Slide 22: 1. Optimize the Site Layout
Preserve and use permeable soils
Limit roofs and paving
Detain and retain runoff throughout the site
Use drainage as a design element
LID CONCEPTS

## Slide 23: 2. Use Pervious Surfaces
Green roofs
Permeable pavements
LID CONCEPTS

## Slide 24: 3. Disperse Runoff
LID CONCEPTS

## Slide 25: 4. Harvest and Reuse Runoff
LID CONCEPTS
Feasibility analysis mandated by permit
Analysis not required if enough runoff can be infiltrated on-site
  80% of long-term runoff
  Requires Ksat ≥ 1.6“/hour (Group A soils)
Simplified criteria submitted to Water Board in Dec. 2011
Feasibility Status Report due Dec. 2014

## Slide 26: Screening for Adequate Demand
Identify and list sub-areas of site from which runoff could feasibly be captured
Calculate on-site demand for:
  Toilet flushing
  Landscape Irrigation
  Other uses
Compare on-site demand to drawdown required given:
  80% of runoff to be used
  50,000 gal. storage/acre impervious area
LID CONCEPTS

## Slide 27: Required Demand
Reuse (80% of total)
50,000 gallons storage
(for example, about 25' diameter x 14' high)
30+ years of hourly runoff from one acre
Overflow (20% of total)
Table 4-3 on page 41 | 
Rain Gauge | Min. Demand (gal/day/acre)
Berkeley | 5900
Brentwood | 4200
Martinez | 5900
Dublin | 4100
LID CONCEPTS

## Slide 28: Select Roofs or other Surfaces
“List specific impervious areas from which runoff might be feasibly captured or stored.
All contiguous roof areas 10,000 SF and greater must be listed.”
Page 40

## Slide 29: Default Toilet Flushing Use
Land Use Type | User Unit | User Unit Factor (Optional—use project-specific data if available) | Daily Use/Unit (gal./day/ user unit)*
Residential | Resident | 2.8 residents/ dwelling unit | 8.6
Office or Retail | Employee (non-visitor) | 200 SF/ employee | 6.9
Schools | Employee (does not include students) | 50 SF/ employee | 33.9
Industrial Uses (not including process water) | Employee (non-visitor) |  | 5.4
*Or use project-specific data
LID CONCEPTS

## Slide 30: Mixed Use Development
LID CONCEPTS
A | B | C | D | E | F | G | H | I | J
Area | SF | Acres | Uses and User Units | Toilet and Urinal Usage (gal/day) | Water Use per Acre | Req’d Demand per Acre | F>G? | Adjacent pervious area ≥ 2.5  “B”? | Other Use ≥ “G”?
B-1 | 21000 | 0.48 | 77 DUs + 9000 SF Retail | 1854 + 310 = 2164 | 4508 | 5900 | No | No | No
77 DUs  2.8 residents/DU  8.6 gal/day/resident = 1854 gal/day
9000 SF retail  200 SF/employee  6.9 gal/day/employee = 310 gal/day
Page 41

## Slide 31
A | B | C | D | E | F | G | H | I | J
Area | SF | Acres | Uses and User Units | Toilet and Urinal Usage (gal/day) | Water Use per Acre | Req’d Demand per Acre | F>G? | Adjacentpervious area ≥ 2.5  “B”? | Other Use ≥ “G”?
All | 41102 | 0.94 | 23 DUs | 554 | 589 | 5900 | No | No | No
Bldgs | 18975 | 0.44 | 23 DUs | 554 | 1271 | 5900 | No | No | No
Bldg A | 4125 | 0.09 | 23 DUs | 554 | 5850 | 5900 | No | No | No
23 DUs x 2.8 residents/DU x 8.6 gal/day/resident = 553.8 gal/day
554 gal/day  .94 acres = 589 gal/day/acre

## Slide 32: Design for Water Supply
Reuse (<<80% of total)
Less storage (<<50,000 gallons/acre)
30+ years of hourly runoff from one acre
More Overflow (>>20% of total)
LID CONCEPTS

## Slide 33: Bioretention in Series

## Slide 34: LID Design Process
LID CONCEPTS
Analyze Project for LID
Develop and Document LID Drainage Design
Specify LID Preliminary Design Details
Coordinate with Site Design and Landscape Design
Page 35

## Slide 35: Analyzing a Project for LID
Five LID Strategies
Optimize the site layout
Use pervious surfaces
Disperse runoff
Store runoff and use it later
Direct runoff to bioretention facilities
LID CONCEPTS

## Slide 36: 5. Direct Runoff to Bioretention
LID CONCEPTS

## Slide 37: Drainage Management Areas
Stormwater NPDES Compliance for New Developments

## Slide 38: LID Site Design Principles
Paved or Roof Area
DMAs

## Slide 39: LID Site Design Principles
DMAs

## Slide 40: LID Site Design Principles
Mimic natural hydrology
Disperse runoff
Keep drainage areas small
Don’t concentrate runoff
Don’t allow run-on from landscaped or natural areas

## Slide 41: Drainage Management Areas
DMAs

## Slide 42: Drainage Management Areas
DMA 1
DMA 2
DMA 3
DMA 4
DMAs

## Slide 43: Drainage Management Areas
DMAs

## Slide 44: Drainage Management Areas
DMAs
Landscaped
Natural
Paved
DMA-5
DMA-7
DMA-6
DMA-8

## Slide 45: Drainage Management Areas
DMAs
Landscaped
Natural
Paved
DMA-5
DMA-7
DMA-6
DMA-8
Possible Facility Locations
Municipal Storm Drain

## Slide 46: Options – Pervious DMAs
DMAs
DMA-8
  Self-treating?
  Self-retaining?
  Drain to IMP?

## Slide 47: DMA 8
DMAs
Self-Treating
  Drain directly to storm drain system
Self-Retaining
  Retain first inch of rainfall without producing runoff
Drain to IMP
  Use runoff factor to account for contribution
Best choice may depend on slope and relative elevation

## Slide 48: Details
DMAs
Use a curb to avoid run-on from self-treating areas
Grade self-retaining areas to drain inward. Set any area drains to pond 3"-4"
Consider that adjacent roofs or paved areas could drain to self-retaining areas (not to exceed 1:1)
To storm drain

## Slide 49: Options – Combining DMAs
DMAs
Option to combine DMAs if they have identical runoff factors (for example, roofs and paving) and drainage is routed to the same location.
Carefully follow grade breaks and roof ridges to delineate DMAs

## Slide 50: Roof ridges and grade breaks
DMAs

## Slide 51: Roof and Grading Plans
DMAs

## Slide 52: Reviewing Stormwater Control Plans
Stormwater NPDES Compliance for New Developments

## Slide 53: Contents
Project Data
Setting
Low Impact Design Strategies
  Optimization of Site Layout
  Use of Permeable Pavements
  Dispersal of Runoff to Pervious Areas
  Feasibility of Harvesting and Use
Documentation of Drainage Design
Source Control Measures
Stormwater Facility Maintenance
Construction Plan C.3 Checklist
Certifications
REVIEW PLANS

## Slide 54: Impervious Areas Pre/Post
SITE
Reduced Re-Graded Lot
REVIEW PLANS
New Building

## Slide 55: Special Projects
Project Categories
  A
  B
  C
Percent LID and non-LID treatment
Other Reporting Requirements
  Narrative on LID Feasibility
  Criteria used for non-LID facilities
Contact Program Staff for assistance
Page 60
REVIEW PLANS

## Slide 56: Setting and Strategies
Setting
  Project Location and Description
  Existing Site Features and Conditions
  Opportunities and Constraints
LID Strategies
  Optimization of Site Layout
  Use of Permeable Pavements
  Dispersal of Runoff to Pervious Areas
  Feasibility Assessment of Harvesting/Use
  Integrated Management Practices (bioretention)
REVIEW PLANS

## Slide 57: Drainage Design Calculations
Drainage Management Areas |  | 
DMA Name | Surface Type | Area in SF
Σ(DMAs + Bioretention Facilities) = Total Site
REVIEW PLANS

## Slide 58: Example Site
REVIEW PLANS
Landscaped
Natural
Paved
DMA-5
DMA-7
DMA-6
DMA-8
Possible IMP Locations
Municipal Storm Drain

## Slide 59: Example Site
Landscaped
Natural
Paved
DMA-4
DMA-5
DMA-6
DMA-8
Possible IMP Locations
Municipal Storm Drain
1300 SF
1300 SF
1050 SF
1050 SF
4000 SF
5570 SF
7025 SF
9350 SF

## Slide 60: Example Site
REVIEW PLANS
Landscaped
Natural
Paved
DMA-5
DMA-7
DMA-6
DMA-8
Possible IMP Locations
Municipal Storm Drain
1300 SF
1300 SF
1050 SF
1050 SF
4000 SF
5570 SF
7025 SF
9350 SF

## Slide 61: Setting Up Calculations
REVIEW PLANS
Self-retaining Area
Area Draining to Self-retaining Area
DMA Name | Square Feet
DMA-8 | 9350
DMA | Square Feet | Surface | Runoff Factor | Product | Receiving DMA | Receiving Area | Ratio
DMA-1 | 1300 | Roof | 1.0 | 1300 | DMA-8 | 9350 | 0.139

## Slide 62: Setting Up Calculations
REVIEW PLANS
Areas Draining to IMPs
DMA | Area | Surface | Runoff Factor | Area  Runoff Factor | Soil Type |  |  | 
DMA-2 | 1050 | Roof | 1.0 | 1050 | D |  |  | 
DMA-4 | 1300 | Roof | 1.0 | 1300 |  |  |  | 
DMA-7 | 7025 | Paved | 1.0 | 7025 |  |  |  | 
 |  |  |  |  | IMP Sizing Factor | Rain Adjust Factor | Min Area or Volume | Proposed Area or Volume
 |  |  |  | A |  |  |  | 
 |  |  |  | V1 |  |  |  | 
 |  |  |  | V2 |  |  |  | 
 |  |  |  | Orifice Size: |  |  |  | 

## Slide 63: Setting Up Calculations
REVIEW PLANS
Areas Draining to IMPs
DMA | Area | Surface | Runoff Factor | Area x Runoff Factor | Soil Type |  |  | 
DMA-2 | 1050 | Roof | 1.0 | 1050 | D |  |  | 
DMA-4 | 1300 | Roof | 1.0 | 1300 |  |  |  | 
DMA-7 | 7025 | Paved | 1.0 | 7025 |  |  |  | 
 |  |  |  | 9375 | IMP Sizing Factor | Rain Adjust Factor | Min Area or Volume | Proposed Area or Volume
 |  |  |  | A | 0.06 | 1.0 | 562.5 | 
 |  |  |  | V1 | 0.04 | 1.0 | 375.0 | 
 |  |  |  | V2 | 0.05 | 1.0 | 468.8 | 
 |  |  |  | Orifice Size: |  |  |  | 

## Slide 64: Example Site
REVIEW PLANS
IMP-1 1400 SF
Natural
Paved
DMA-5
DMA-7
DMA-6
DMA-8
Municipal Storm Drain
1300 SF
1300 SF
1050 SF
1050 SF
4000 SF
5570 SF
7025 SF
9350 SF

## Slide 65: Setting Up Calculations
REVIEW PLANS
Areas Draining to IMPs
DMA | Area | Surface | Runoff Factor | Area x Runoff Factor | Soil Type |  |  | 
DMA-2 | 1050 | Roof | 1.0 | 1050 | D |  |  | 
DMA-4 | 1300 | Roof | 1.0 | 1300 |  |  |  | 
DMA-7 | 7025 | Paved | 1.0 | 7025 |  |  |  | 
 |  |  |  | 9375 | IMP Sizing Factor | Rain Adjust Factor | Min Area or Volume | Proposed Area or Volume
 |  |  |  | A | 0.06 | 1.0 | 562.5 | 1400
 |  |  |  | V1 | 0.04 | 1.0 | 375.0 | 400
 |  |  |  | V2 | 0.05 | 1.0 | 468.8 | 475
 |  |  |  | Orifice Size: |  |  |  | 0.6 in.

## Slide 66: Source Control Measures
Page 28

## Slide 67
REVIEW PLANS
Page 29

## Slide 68: Stormwater Facility Maintenance
Ownership and responsibility
  Commitment to execute agreements
  Accept O&M until formally transferred
Maintenance requirements
  Fact sheets on website
Page 29
REVIEW PLANS

## Slide 69: Construction C.3 Checklist
REVIEW PLANS
Page 32

## Slide 70: Certification
“The selection, size, and preliminary design of treatment BMPs and other control measures in this plan meet the requirements of Regional Water Quality Board Order R2-2009-0074.”

## Slide 71: Reporting

## Slide 72: Small Projects
Stormwater NPDES Compliance for New Developments

## Slide 73: Provision C.3.i.
Started December 1, 2012
Small Projects
  All projects requiring approvals or permits
  2,500 SF ≥ impervious area ≤10,000 SF
  Single family homes ≥ 2,500 SF
Site Design Measures
  Rain barrels or cisterns
  Direct runoff to vegetated areas
  Permeable pavement
Develop standard specifications
Reporting: Discuss implementation
SMALL

## Slide 74
SMALL

## Slide 75: Bioretention Design
Stormwater NPDES Compliance for New Developments

## Slide 76: Make This Happen
BIORETENTION
Bioretention facilities are level so they “fill up like a bathtub.”

## Slide 77
Page 76

## Slide 78: Outlets
BIORETENTION
Overflow elevation
Page 76

## Slide 79: Bioretention Edges
Page 77
BIORETENTION

## Slide 80: DMAs with Grading Shaded
BIORETENTION

## Slide 81: Call out elevations
BIORETENTION
    Outlet structure
  Top of overflow grate
  Underdrain connection
    Inlet
  Flow line at inlet
  Top of curb
  Top of adjacent paving
    Soil layers
  Top of soil layer
  Bottom of gravel layer
  Bottom of soil layer

## Slide 82: Gravel and Underdrain
BIORETENTION
    Class 2 permeable
  Caltrans spec 68-1.025
  Typical to be slightly off gradation spec on delivery
    No filter fabric
    Underdrain
  Near top of gravel layer
  PVC SDR 35 or equivalent; holes facing down
  Solid pipe for 2' closest to outlet structure
  Cleanout

## Slide 83: Soil Specification
    60-70% Sand
  ASTM C33 for fine aggregate
    30-40% Compost
  Certified through US Composting Council Seal of Testing Assurance Program
    Submittal per Guidebook
    Option to accept test results for a “brand-name” mix if volume is less than 100 cubic yards
    Install in 8"-12" lifts
    Do not compact
    Do not overfill
    Leave room for mulch
BIORETENTION

## Slide 84: Bioretention Construction
Runoff flow from the intended tributary drainage management area must flow into the facility.
The surface reservoir must fill to its intended volume during high inflows.
Runoff must filter rapidly through the layer of imported soil mix.
Filtered runoff must infiltrate into the native soil to the extent possible (or allowable).
Remaining runoff must be captured and drained to a storm drain or other approved location.
Page 95
BIORETENTION

## Slide 85: Plantings
BIORETENTION
    Maintain design top of soil elevation
    Trees
  Incorporate into bioretention facility
  Account for surface roots

## Slide 86: Pedestrian Access, Utilities
BIORETENTION

## Slide 87: Operation & Maintenance
Stormwater NPDES Compliance for New Developments

## Slide 88: Ensure Operation & Maintenance
Initial inspection within 45 days
Inspect 20% of facilities each year
Inspect every facility once every 5 years
O&M

## Slide 89: What to look for
Properly designed and constructed bioretention facilities are nearly maintenance-free…
…Unless facilities are treated as ordinary landscaping.
  Additions of topsoil or mulch
  Re-grading
  Additional plantings
Also…
  Plants may grow so dense that runoff can’t enter
O&M

## Slide 90: Addition of material

## Slide 91: Resources for O&M Inspections
Forms
  Designation of Responsible Individuals
  Operation and Maintenance Log
O&M Fact Sheets
Example O&M Plans
  Example Contents of Inspector’s Report
O&M

## Slide 93: Discussion