## Slide 1: Grading & Drainage Design
for Bioretention Facilities
Dan Cloak Environmental Consulting May 23, 2011

## Slide 2: Overview
Consider drainage early in the design process
Find suitable sites for bioretention
    Use roof plans and grading/paving plans to analyze and display drainage management areas
Distribute bioretention through the site
Grade to distribute drainage to among inlets
    Use the head from roof leaders to move roof runoff
    Avoid utility conflicts

## Slide 3: Consider Drainage Early

## Slide 4: Suitable Sites
Find suitable sites for bioretention
    Downgradient
    Unbuildable
    Aesthetic

## Slide 5: Roof and Grading Plans
Drainage area includes portions of roof and of parking lot

## Slide 6: Distribute through the site
    Facilitates mimicking pre-development hydrology of site
    Keeps drainage runs short and shallow
    Avoid creating barriers to circulation

## Slide 7: Distribute throughout site

## Slide 8: Distribute throughout site
    On steep sites consider:
    Integrating bioretention facilities with terracing
    Collecting runoff in the conventional way and piping to bioretention facilities at the base of the slope

## Slide 9: Distribute runoff
    Avoid conventionally swaled pavement

## Slide 10: Tightline Roof Leaders
    Use the head from roof leaders to move roof runoff

## Slide 11: Utility Conflicts
    Avoid conflicts with existing underground utilities
    Avoid conflicts with newly installed utilities