## Slide 1: C.3 in MRP 2.0
What to Expect (as of March 17, 2015)
Dan Cloak

## Slide 2: What’s Unlikely to Change
Threshold for Regulated Projects
Requirements for Small Projects
Exclusions, including those for roads
50% Rule
Alternative compliance
Ambiguities related to applicability
Organization of permit provision
Reporting (except for Special Projects)

## Slide 3: MRP 2.0: What’s Likely to Change
Design specs for pervious pavement
Operation and maintenance verification
  Apply to pervious pavements
  Enforcement response plan required
Green Infrastructure Plan

## Slide 4: Still under discussion (as of 3/17)
Grandfathering
Infiltration and Harvest/Reuse Feasibility
Soil Specification (Attachment L)
Hydromodification Management
Special Projects
  Intention to eliminate in next permit term
  Tweaks to definitions of density required
  More explicit analysis of bioretention feasibility

## Slide 5: Stormwater Control Plans
What to Look for During Your Review
Dan Cloak

## Slide 6: Four Questions for SCP Review
Does it meet Provision C.3 requirements?
  All impervious areas accounted for?
  Features and facilities adequately sized?
  Facilities properly designed?
Is it congruent with the project design?
  Site Plan
  Grading and Drainage Plan
  Landscaping Plan

## Slide 7: Four Questions for SCP Review
Is it buildable?
  Slopes
  Soils
  Setbacks and allowable uses
  Other project requirements
Is it the best design for this project?
  Most effective stormwater treatment
  Cost effective and maintainable
  Best for municipality and community

## Slide 8: Exhibit
Entire site divided into DMAs
Locations and sizes of LID facilities

## Slide 9: Drainage Management Areas

## Slide 10: Surface Drainage

## Slide 11: Before Entitlements
Delineation of DMAs is consistent with preliminary grading and drainage design
Each bioretention facility is level and flat
Facilities are shown in artist renderings
Facilities do not create conflicts with vehicle and pedestrian circulation
Landscaping plans show bioretention facilities with appropriate plant palette

## Slide 12: Bioretention Facilities
What to Look for During Plan Check
Dan Cloak

## Slide 13: Revisions to Preliminary Plans
Site Plan
Grading and Drainage Plan
Landscaping Plan

## Slide 14
Page 76
Bioretention Design Specs

## Slide 15: Bioretention Functions
infiltration
evapotranspiration
Discharge
(biotreatment)
losses

## Slide 16: Flat with raised underdrain
Or this
Not this

## Slide 17: Elevations

## Slide 18: Overflow Elevation
Overflow elevation

## Slide 19: Underdrain Elevation

## Slide 20: Protection of Adjacent Structures

## Slide 21: Utilities

## Slide 22: Discussion

## Slide 23: Inspecting Construction of Bioretention Facilities
Carlton Thompson and Jeff Cowling

## Slide 24: Reviewing Bioretention Soil Submittals
Dan Cloak, Carlton Thompson, and Jeff Cowling

## Slide 25: Background
On the bioretention soil specification
Dan Cloak

## Slide 26: Soil Specifications Milestones
Early bioretention specifications called for “sandy loam” with a minimum infiltration rate of 5"/hr.
Municipal staff developed a “bucket test” and then the “dirt bong” to check the infiltration rate
Staff encountered difficulty obtaining consistent and repeatable results from test

## Slide 27: Soil Specifications Milestones
More consistent results could be obtained by an engineered soil (sand/compost mix)
Contra Costa developed and refined a specification (2008)
MRP 1.0 (2009) required development of a soil specification for all Permittees
Regional roundtable recommended Contra Costa’s mix
Specification added to permit (2011)

## Slide 28: Soil Specifications Milestones
Permit Attachment L allows municipalities to accept a “brand-name” mix in lieu of site-specific testing
CCCWP invited soil suppliers to submit samples and lab results for “brand name” mixes and be listed on website
Some municipalities are using the bucket test or dirt bong to field-test delivered mix